## Slide 1
History of and Recent Advances in Designing Soil Nail Walls
September 20, 2023
HOAG HOSPITAL – NEW PORT BEACH, CA.

## Slide 2
    Agenda
    Soil Nailing – History +Insight
      History – Prof. Shen/Larry Kulchin
      Prof. Vucetic – Bi-Linear Failure Plane
    2. Recent Advances
      Post Tensioned Soil Nailing
      V-Nails
      Hybrid Soil Nailing
      Optimization

## Slide 3
  Past Experience Designs of Structures
  Skidmore, Owings and Merrill - SOM
  March 1968
Buildings

## Slide 4
Soil Nailing History
1st. Soil Nail Wall Built in the US (1978)
Early Soil Nail Wall by PB&A – EBMUD in Oakland, CA (1985)

## Slide 6
Richard K. Eamer Medical Center, USC Campus
1st Permanent Soil Nail Wall in the United States
Circa - 1986

## Slide 8
Glendale Adventist Medical Center –Acute Care Facility

## Slide 9
OSHPD = HCAI
Alternate Method of Compliance
Aug. 21, 2006
www.pbandainc.com/wp-content/uploads/2013/07/oshpd.pdf
DATE 04/25/00

## Slide 12
    Agenda
    Soil Nailing – History +Insite
      History – Prof. Shen/Larry Kulchin
      Prof. Vucetic – Bi-Linear Failure Plane
    2. Recent Advances
      Post Tensioned Soil Nailing
      V-Nails
      Hybrid Soil Nailing
      Optimization

## Slide 13
Caquinez
Bridge
Shoring
Before and after
North Anchorage
=======
Post-Tensioned
Soil nailing

## Slide 15
F.O.S =1.2
F.O.S =1.356

## Slide 16
 | Nail Length in Original Design (ft) | Nail Length needed to achieve FoS of 1.351 (ft) | Difference in Length (ft) |  | 
Nail 1 | 80 | 115 | 35 |  | 
Nail 2 | 80 | 105 | 25 |  | 
Nail 3 | 80 | 100 | 20 |  | 
Nail 4 | 80 | 95 | 15 |  | 
Nail 5 | 75 | 90 | 15 |  | 
Nail 6 | 75 | 80 | 5 |  | 
Nail 7 | 70 | 70 | 0 |  | 
Nail 8 | 60 | 60 | 0 |  | 
Nail 9 | 50 | 50 | 0 |  | 
Nail 10 | 40 | 40 | 0 |  | 
Nail 11 | 30 | 30 | 0 |  | 
 |  | Total | 115 |  | 

## Slide 17
3. Mobilized shear approach (prestressed nails):
- Run slope stability analysis considering applicable prestress force
- Determine force equilibrium in every slice with the prestress force (.p in equation below)
- Determine remaining available nail shear resistance (Design Ultimate – prestress) at each slice without satisfying force equilibrium
W
Nail R
Wx
Rx
Ry
Wy
1. General slope stability:
- General limit equilibrium approach
- Include all forces in slice
- Determine force equilibrium in every slice
- Large nail forces might turn sliding mode into passive (showing smaller FS)
2. Mobilized shear approach (passive nails):
- Passive nails are reactionary
- Without nails, determine safety factors, available soil shear resistance, and required shear resistance for a safety factor of one
- Determine available nail shear resistance at each slice without satisfying force equilibrium

## Slide 18
    Agenda
    Soil Nailing – History +Insite
      History – Prof. Shen/Larry Kulchin
      Prof. Vucetic – Bi-Linear Failure Plane
    2. Recent Advances
      Post Tensioned Soil Nailing
      V-Nails
      Hybrid Soil Nailing
      Optimization

## Slide 19
Carroll Canyon DAR – I-805 – San Diego
Use of V-Nails For Retention of Live Highway
Internal Bracing – Designed by T.Y. Lin
805-S
805-N
HOV

## Slide 22
V-NAILS

## Slide 23
V-NAILS
I-805 N
I-805 N

## Slide 26
Brookfield, CT. US-7

## Slide 27
    Agenda
    Soil Nailing – History +Insite
      History – Prof. Shen/Larry Kulchin
      Prof. Vucetic – Bi-Linear Failure Plane
    2. Recent Advances
      Post Tensioned Soil Nailing
      V-Nails
      Hybrid Soil Nailing
      Optimization

## Slide 30
Hybrid Wall
Finite Element Analysis of Hybrid Wall with staged construction for “Jamul Casino Extension”

## Slide 31
    Agenda
    Soil Nailing – History +Insite
      History – Prof. Shen/Larry Kulchin
      Prof. Vucetic – Bi-Linear Failure Plane
    2. Recent Advances
      Post Tensioned Soil Nailing
      V-Nails
      Hybrid Soil Nailing
      Optimization

## Slide 32
    The Height

## Slide 33
Soil Nail Optimization
For each soil nail, three factors are considered in the evaluation of the overall FOS of the wall:
Factor 1 – Punching shear plus pullout strength of the length of the nail in front of the failure plane.
Factor 2 – Yield strength of the soil nail,
Factor 3 – Pull out the strength of the soil nail length behind the failure plane
THE CONTRIBUTION OF EACH NAIL IS THE MINIMUM OF THE ABOVE 3 FACTORS.

## Slide 34
Soil Nail Optimization

## Slide 35
Soil Nail Optimization
Original Design
PB&A Design

## Slide 36
Soil Nail Optimization
Original Design
PB&A Design
Row # | L (ft) | Size
1 | 82 | #14
2 | 82 | #14
3 | 82 | #14
4 | 82 | #14
5 | 82 | #14
6 | 78 | #14
7 | 78 | #14
8 | 78 | #14
9 | 75 | #14
10 | 68 | #18
11 | 68 | #18
12 | 68 | #18
13 | 68 | #18
14 | 60 | #14
15 | 60 | #14
16 | 55 | #14
17 | 45 | #14
18 | 40 | #14
19 | 40 | #14
Row # | L (ft) | Size
1 | 75 | #10
2 | 70 | #10
3 | 70 | #10
4 | 70 | #10
5 | 70 | #10
6 | 65 | #10
7 | 65 | #10
8 | 65 | #10
9 | 65 | #18
10 | 60 | #18
11 | 60 | #18
12 | 60 | #18
13 | 60 | #18
14 | 50 | #14
15 | 40 | #14
16 | 30 | #14
17 | 25 | #14
18 | 20 | #14
19 | 15 | #14
Row # | Diff. in Length (ft)
1 | 7
2 | 12
3 | 12
4 | 12
5 | 12
6 | 13
7 | 13
8 | 13
9 | 10
10 | 8
11 | 8
12 | 8
13 | 8
14 | 10
15 | 20
16 | 25
17 | 20
18 | 20
19 | 25
Total | 256
Length Optimization per 1 column of nails

## Slide 37
Soil Nail Optimization
Original Design
PB&A Design
17’’+/- total facing thickness for entire wall height
10 to 18’’ total facing thickness varies based on wall height

## Slide 38
Soil Nail Optimization
“Top to bottom, PB&A was able to reduce the length of the soil nails by 44 percent”
“PB&A’s optimized design reduced the overall weight of the required steel by 65 percent.”
“The soil nail-facing optimization resulted in a 23 percent reduction in concrete over the entire length of the project.”
“PB&A's design optimization saved approximately $2,000,000 (of a total of $7,000,000) in construction costs and improved construction scheduling and productivity.”